## Slide 1: Paper III Digital Electronics and Microprocessor UNIT – I Logic Gates & Logic Families
ONLINE / LIVE TEACHING CLASSES
SESSION 2020-2021
DATE: 6 February 2021

## Slide 2: Unit I – Logic Gates & Logic Families
Logic Gates: Symbol, diode/transistor switch circuit and logical expression, truth table of basic gates (AND, OR, NOT), Universal gates (NAND, NOR) and special purpose gates (Ex-OR, Ex-NOR), Tristate Logic.
2

## Slide 3: Logic Gates & Logic Families
3

## Slide 4: Unit Outcomes
Develop basic gates using the given NAND/NOR gates as universal gates.
Simplify the given expression using Boolean Expression.
Develop logic circuits using the given Boolean expressions.
Compare the salient characteristics of the given digital logic families.
4

## Slide 5: Unit II – Logic Gates & Logic Families
Logic Gates: Symbol, diode/transistor switch circuit and logical expression, truth table of basic gates (AND, OR, NOT), Universal gates (NAND, NOR) and special purpose gates (Ex-OR, Ex-NOR), Tristate Logic.
5

## Slide 6: Basics…..
Logic gates are the fundamental building blocks of digital systems.
The name logic gate is derived from the ability of such devices to make decisions, in the sense that it produces one output level when some combinations of input levels are present
6

## Slide 7: Basics…..
Inputs & Outputs for Logic Circuits
  Input & Output of logic gates can occur only in two levels.
HIGH
True ON 1
LOW
False OFF 0
7

## Slide 8: Basics…..
Truth Table
  A table which lists all the possible combinations of input variables and the corresponding outputs is called a “Truth Table”.
  It shows how the logic circuits output responds to various
combinations of logic levels at the inputs
23
Switches in parallel => OR
Switch 1 | Switch 2 | Output
OFF | OFF | OFF
OFF | ON | GLOW
ON | OFF | GLOW
ON | ON | GLOW

## Slide 9: Basics…..
Logic
  A logic in which the voltage levels represent logic 1 and logic 0.
  Level logic may be Positive or Negative.
  A “Positive Logic” is the one which the higher of the two voltage levels represents the logic 1 and the lower of the two voltage level represents the logic 0.
  A “Negative Logic” is the one which the lower of the two voltage levels represents the logic 1 and the higher of the two voltage level represents the logic 0.
9

## Slide 10: Basics…..
Logic
  Positive Logic
Logic 0 (LOW)=0V
Logic 1 (HIGH)=+5V
  Negative Logic
Logic 0 (LOW)=+5V
Logic 1 (HIGH)=0V
10

## Slide 11: Logic Gates
Logic Gates
Basic Gates
Universal Gates
Special Purpose Gates
AND Gate OR Gate NOT Gate
NAND Gate NOR Gate
Ex-OR Gate Ex-NOR Gate
11

## Slide 12
AND Gate
An AND gate has two or more inputs but only one output.
The output assumes the logic 1 state, when both inputs are at logic 1 state.
The output assumes the logic 0 state even if one of its inputs is at logic 0 state.
27
A
B
Y=A.B
Logic Symbol

## Slide 13: AND Gate
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
13
A
B
0
0
Y=A.B
0

## Slide 14: AND Gate
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
14
A
B
0
1
Y=A.B
0

## Slide 15: AND Gate
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
15
A
B
1
0
Y=A.B
0

## Slide 16: AND Gate
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
16
A
B
1
1
Y=A.B
1

## Slide 17: Realization of AND Gate using Diode
D2
17
+5V
R
D1
Output
A
B

## Slide 18: Realization of AND Gate using Diode
D2
Output = 0
A = 0
B = 0
Case I: When A = 0 and B = 0
+5V
R
D1
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
 |  | 33

## Slide 19: Realization of AND Gate using Diode
D2
Output = 0
A = 0
B = 1
Case II: When A = 0 and B = 1
+5V
R
D1
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
 |  | 34
+5V

## Slide 20: Realization of AND Gate using Diode
D2
Output = 0
A = 1
B = 0
Case III: When A = 1 and B = 0
+5V
R
D1
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
 |  | 35
+5V

## Slide 21: Realization of AND Gate using Diode
D2
Output = 1
A = 1
Case IV: When A = 1 and B = 1
+5V
R
D1
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 316
+5V
+5V
B = 1

## Slide 22: Realization of AND Gate using Transistor
37
+5V
R
Output
A
B
R
R
R
R
Q1
Q2
Q3

## Slide 23: Realization of AND Gate using Transistor
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
 |  | 38
R
Output = 0
A
B
R
R
R
R
Q2
Case I: When A = 0 and B = 0
+5V
Q1
OFF
OFF
Q3
ON
+
-
VBE>0.7
BE
V <0.7
VBE<0.7

## Slide 24: Realization of AND Gate using Transistor
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
 |  | 39
R
Output = 0
A
B
R
R
R
R
Q2
Case II: When A = 0 and B = 1
+5V
Q1
OFF
ON
Q3
ON
+
-
+5V
+
-
VBE>0.7
VBE>0.7
VBE<0.7

## Slide 25: Realization of AND Gate using Transistor
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
 |  | 40
R
Output = 0
B
R
R
R
R
Q2
Case III: When A = 1 and B = 0
+5V
Q1
ON
OFF
Q3
ON
+
-
A+5V
+
-
VBE>0.7
VBE>0.7
VBE<0.7

## Slide 26: Realization of AND Gate using Transistor
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 411
R
Output = 1
R
R
R
R
Q2
Case IV: When A = 1 and B = 1
+5V
Q1
ON
ON
Q3
OFF
+
-
A+5V
+
-
VBE>0.7
VBE>0.7
VBE<0.7
+5V
B

## Slide 27: 3 - Input AND Gate
A B
Y1=A.B
Y=Y1.C
=A.B.C
C
A B
C
27
Y=A.B.C
Input |  |  | Output Y=A.B.C
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Symbol : 3 – Input AND Gate
Truth Table : 3 – Input AND Gate
3 – Input AND Gate using 2 – Input AND Gate

## Slide 28: AND Gate IC – IC 7408 (Quad 2 I/P AND Gate)
This device contains four independent gates each of which performs the logic AND function.
Pin Configuration of IC 7408
Function Table of IC 7408
28

## Slide 29: Verification of AND Gate IC 7408
+5V
R 330Ω
29

## Slide 30: Verification of AND Gate IC 7408
Double check the pin numbers when working with ICs.
1
7
8
14
30

## Slide 31: Verification of AND Gate IC 7408
VCC
A
B
GND
31

## Slide 32: OR Gate
An OR gate has two or more inputs but only one output.
The output assumes the logic 1 state, when even if one of its inputs is in logic 1 state.
The output assumes the logic 0 state only when both the inputs are in logic 0 state.
A
B
Y=A+B
Logic Symbol

## Slide 33: OR Gate
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
A
B
0
0
Y=A+B
0
33

## Slide 34: OR Gate
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
A
B
0
1
Y=A+B
1
34

## Slide 35: OR Gate
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
A
B
1
0
Y=A+B
1
35

## Slide 36: OR Gate
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A
B
1
1
Y=A+B
1
36

## Slide 37: Realization of OR Gate Using Diodes
D1
D2
R
Output
A
B
37

## Slide 38: Realization of OR Gate Using Diodes
D1
D2
R
Output =0
A=0
B=0
Case I: When A = 0 and B = 0
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
38

## Slide 39: Realization of OR Gate Using Diodes
D1
D2
R
Output = 1
A=0
B=1
Case II: When A = 0 and B = 1
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
+5V
39

## Slide 40: Realization of OR Gate Using Diodes
D1
D2
R
Output = 1
A=1
B=0
Case III: When A = 1 and B = 0
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
+5V
40

## Slide 41: Realization of OR Gate Using Diodes
D1
D2
Output = 1
A=1
Inputs |  | Output
A | B | Y=A+B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 516
Case IV: When A = 1 and B = 1
+5V
B=1
+5V
R

## Slide 42: Realization of OR Gate Using Transistors
57
+5V
R
Output
A
R
R
B
R
Q1
Q2
Q3

## Slide 43: Realization of OR Gate Using Transistors
+5V
R
Output = 0
A=0
B=0
R
R
R
Q1
Q2
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
 |  | 58
OFF
Q3
ON
+
-
BE
V >0.7
VBE<0.7
BE
V <0.7 OFF
Case I: When A = 0 and B = 0

## Slide 44: Realization of OR Gate Using Transistors
+5V
R
Output = 1
A=0
B=1
R
R
Q1
Q2
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 1
 |  | 59
OFF
ON
+
-
VBE>0.7
VBE<0.7
R
Q3
VBE<0.7 OFF
Case II: When A = 0 and B = 1
+5V

## Slide 45: Realization of OR Gate Using Transistors
+5V
R
Output = 1
A=1
B=0
R
R
Q1
Q2
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
 |  | 60
+
-
VBE<0.7 OFF
Q3
VBE<0.7 OFF
Case III: When A = 1 and B = 0
+5V VBE>0.7 ON
R

## Slide 46: Realization of OR Gate Using Transistors
+5V
R
Output = 1
A=1
B=1
R
R
Q1
Q2
Inputs |  | Output
A | B | Y=A.B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 611
+
-
Q3
VBE<0.7 OFF
Case IV: When A = 1 and B = 1
+5V VBE>0.7 ON
R
VBE>0.7 ON

## Slide 47: Three Input OR Gate
A
B
Y1=A+B
Y=Y1+C
=A+B
A
B
C
47
Input |  |  | Output Y=A+B+C
A | B | C | Y
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
C
Symbol : 3 – Input OR Gate
Truth Table : 3 – Input OR Gate
3 – Input OR Gate using 2 – Input OR Gate
Y=A+B+C

## Slide 48: OR Gate IC – IC 7432 (Quad 2 I/P OR Gate)
This device contains four independent gates each of which performs the logic OR function
Pin Configuration of IC 7432
Function Table of IC 7432
48

## Slide 49: NOT Gate (Inverter)
64
A
A NOT gate, also called inverter, has only one input and of course only one output.
It is a device whose output is always the complement of its input.
That is, the output of a NOT gate assumes the logic 1 state when its input is in logic 0 state and vice versa.
−
Y = A
Logic Symbol

## Slide 50: NOT Gate
A
0
−
50
Y = A
1
Input | Output
A | − Y = A
0 | 1

## Slide 51: NOT Gate
A
1
−
51
Y = A
0
Input | Output
A | − Y = A
0 | 1
1 | 0

## Slide 52: Realization of NOT Gate using Transistor
+5V
A
R
R
Output
Q1
52

## Slide 53: Realization of NOT Gate using Transistor
+5V
A=0
R
R
Output= 1
Input | Output
A | − Y = A
0 | 1
Q1
OFF
VBE<0.7
Case I: When A = 0
53

## Slide 54: Realization of NOT Gate using Transistor
+5V
A=1
R
R
Output= 0
Input | Output
A | − Y = A
0 | 1
1 | 0
Q1 ON
VBE>0.7
Case II: When A = 1
+5V
54

## Slide 55: NOT Gate IC – IC 7404 (Hex Inverters)
This device contains six independent inverters
Pin Configuration of IC 7404
Function Table of IC 7404
55

## Slide 56: Unit II – Logic Gates & Logic Families
Logic Gates: Symbol, diode/transistor switch circuit and logical expression, truth table of basic gates (AND, OR, NOT), Universal gates (NAND, NOR) and special purpose gates (Ex-OR, Ex-NOR), Tristate Logic.
56

## Slide 57
Universal Gates (NAND and NOR Gate)
NAND and NOR gates are Universal Gates.
Both NAND and NOR gates can perform all the three basic logic functions (AND, OR and NOT).
Therefore, AOI logic can be converted to NAND logic or NOR logic
57

## Slide 58: NAND Gate
NAND means NOT AND i.e. AND output is inverted.
So NAND gate is a combination of an AND gate and a NOT gate.
A
B
A.B
AB
A.B
A
B
NAND Gate
AND Gate
NOT Gate
58

## Slide 59
NAND Gate
The output is logic 0 level, only when all the inputs are logic 1 level.
For any other combination of inputs, the output is a logic 1 level.
A
B
Y = A.B
59
Logic Symbol

## Slide 60: NAND Gate
A
B
0
0
Y = A.B
1
Inputs |  | Output
A | B | Y = A.B
0 | 0 | 1
60

## Slide 61: NAND Gate
A
B
0
1
Y = A.B
1
Inputs |  | Output
A | B | Y = A.B
0 | 0 | 1
0 | 1 | 1
61

## Slide 62: NAND Gate
A
B
1
0
Y = A.B
1
Inputs |  | Output
A | B | Y = A.B
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
62

## Slide 63: NAND Gate
A
B
1
1
Y = A.B
0
Inputs |  | Output
A | B | Y = A.B
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
63

## Slide 64: Realization of NAND Gate using Transistor
+5V
R
Output
A
B
D1
R
Q1
D2
64

## Slide 65: 3 - Input NAND Gate
Y = A.B.C
A B C
INPUT |  |  | OUTPUT
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
65

## Slide 66: NAND Gate IC – IC 7400 (Quad 2 I/P NAND Gate)
This device contains
four
independent
gates
each
of
which performs
the logic
NAND function.
Pin Configuration of IC 7400
Function Table of IC 7400
66

## Slide 67: NOR Gate
NOR means NOT OR i.e. OR output is inverted.
So NOR gate is a combination of an OR gate and a NOT gate.
NOR Gate
A
B
Y = A + B
OR Gate
A
B
A + B
NOT Gate
A + B
67

## Slide 68
NOR Gate
The output is logic 1 level, only when all the inputs are logic 0 level.
For any other combination of inputs, the output is a logic 0 level.
Logic Symbol
A
B
Y = A + B
68

## Slide 69: NOR Gate
A
B
0
0
Y = A + B
1
Inputs |  | Output
A | B | Y = A + B
0 | 0 | 1
69

## Slide 70: NOR Gate
A
B
0
1
Y = A + B
0
Inputs |  | Output
A | B | Y = A + B
0 | 0 | 1
0 | 1 | 0
70

## Slide 71: NOR Gate
A
B
1
0
Y = A + B
0
Inputs |  | Output
A | B | Y = A + B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
71

## Slide 72: NOR Gate
A
B
1
1
Y = A + B
0
Inputs |  | Output
A | B | Y = A + B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
72

## Slide 73: Realization of NOR Gate using Transistor
+5V
R
Output
A
R
R
B
Q1
Q2
73

## Slide 74: 3 – Input NOR Gate
Y = A + B + C
A B C
INPUT |  |  | OUTPUT
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
74

## Slide 75: NOR Gate IC – IC 7402 (Quad 2 I/P NOR Gate)
This device contains
Four
independent
gates
each
of
which performs
The logic
NOR function.
Pin Configuration of IC 7402
Function Table of IC 7402
75

## Slide 76: Universal Gate
NOT Gate using NAND Gate
A
A
−
Y = A
......... (A.A=A)
76
Y = A.A
Y = A

## Slide 77: Universal Gate
AND Gate using NAND Gate
A
Y 1 = A.B
B
( A=A )
Y = A.B
Y = A.B
A B
77
Y=A.B

## Slide 78: Universal Gate
OR Gate using NAND Gate
A
B
Y 1 = A
Y 2 = B
( Demorgan's Theorem)
Y = A.B
Y = A + B
Y = A + B
A
B
Y=A+B
78

## Slide 79: Universal Gate
NOR Gate using NAND Gate
A
B
Y 1 = A
Y 2 = B
Y = A + B
Y 3 = A.B
Y 3 = A + B
A
B
Y = A + B
79

## Slide 80: Universal Gate
NOT Gate using NOR Gate
A
A
−
Y = A
Y = A + A
Y = A ......... (A+A=A)
80

## Slide 81: Universal Gate
OR Gate using NOR Gate
A
Y 1 = A + B
B
( A=A )
Y = A + B
Y = A + B
A
B
Y=A+B
81

## Slide 82: Universal Gate
AND Gate using NOR Gate
A
B
Y 1 = A
Y 2 = B
( Demorgan's Theorem)
Y = A+B
Y = A.B
Y = A.B
A B
Y=A.B
82

## Slide 83: Universal Gate
NAND Gate using NOR Gate
A
B
Y 1 = A
Y 2 = B
Y = A.B
Y 3 = A+B Y 3 = A.B
A
B
Y = A.B
83

## Slide 84: Why NAND Logic or NOR Logic?
IC Type | Gates | Gate / IC | # ICs
74LS04 | 1 | 6 | 1
74LS08 | 2 | 4 | 1
74LS32 | 1 | 4 | 1
Total Number of ICs → |  |  | 3
84
IC Type | Gates | Gate / IC | # ICs
74LS02 | 7 | 4 | 2
Total Number of ICs → |  |  | 2
AOI Logic
NOR Logic

## Slide 85: Unit II – Logic Gates & Logic Families
Logic Gates: Symbol, diode/transistor switch circuit and logical expression, truth table of basic gates (AND, OR, NOT), Universal gates (NAND, NOR) and special purpose gates (Ex-OR, Ex-NOR), Tristate Logic.
85

## Slide 86
Special Purpose Gate – Ex-OR Gate
An Ex-OR gate is two input, one output logic circuit.
The output assumes the logic 1 state, when one and only one of its two inputs assumes a logic 1 state.
Under the conditions when both the inputs assume the logic 0 state or logic 1 state, the output assumes logic 0.
86

## Slide 87: Ex-OR Gate
If input variables are represented by A and B and the output variable by Y the representation for the output of this gate is as
A
B
Y = A ⊕ B
87
− −
Y = AB + AB
Logic Symbol
Logic Expression

## Slide 88: Ex-OR Gate
A
B
0
0
Inputs |  | Output
A | B | Y = A ⊕ B
0 | 0 | 0
88
Y = A ⊕ B
0

## Slide 89: Ex-OR Gate
A
B
0
1
Inputs |  | Output
A | B | Y = A ⊕ B
0 | 0 | 0
0 | 1 | 1
89
Y = A ⊕ B
1

## Slide 90: Ex-OR Gate
A
B
1
0
Inputs |  | Output
A | B | Y = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
90
Y = A ⊕ B
1

## Slide 91: Ex-OR Gate
A
B
1
1
Inputs |  | Output
A | B | Y = A ⊕ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
91
Y = A ⊕ B
0

## Slide 92: 3 – Input Ex-OR Gate
Y = A ⊕ B ⊕ C
INPUT |  |  | OUTPUT
A | B | C | Y = A ⊕ B ⊕ C
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1 107
A
B
C
A ⊕ B
Y = A ⊕ B ⊕ C
A B
C

## Slide 93: Ex-OR Gate IC – IC 7486 (Quad 2 I/P Ex-OR Gate)
This device contains
four
independent gates each of which performs the logic XOR function.
Pin Configuration of IC 7486
Function Table of IC 7486

## Slide 94
Special Purpose Gate – Ex-NOR Gate
An Ex-NOR gate is two input, one output logic circuit.
The output assumes a logic 0 state, when one of the input assumes a logic 0 state and other a logic 1 state.
The output assumes a logic 1 state only when both the inputs assume a logic 0 state or when both the inputs assume a logic state.

## Slide 95: Ex-NOR Gate
If input variables are represented by A and B and the output variable by Y the representation for the output of this gate is as
A
B
Y = A B
− −
Y = AB + AB
Logic Symbol
110
Logic Expression

## Slide 96: Ex-NOR Gate
A
B
0
0
Y = A B
1
Inputs |  | Output
A | B | Y = A B
0 | 0 | 1

## Slide 97: Ex-NOR Gate
A
B
0
1
Y = A B
0
Inputs |  | Output
A | B | Y = A B
0 | 0 | 1
0 | 1 | 0

## Slide 98: Ex-NOR Gate
A
B
1
0
Y = A B
0
Inputs |  | Output
A | B | Y = A B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0

## Slide 99: Ex-NOR Gate
A
B
1
1
Y = A B
1
Inputs |  | Output
A | B | Y = A B
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 100: 3 – Input Ex-NOR Gate
A
B
C
A B
Y = A B C
INPUT |  |  | OUTPUT
A | B | C | Y = A B C
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Y = A B C
A B C

## Slide 101: Ex-NOR Gate IC – IC 74266
This device contains
four
independent
gates
each
of
which performs
The logic
XNOR function.
Pin Configuration of IC 74266