## Slide 1: Instruction set of 8086 Microprocessor

## Slide 2: Software
The sequence of commands used to tell a microcomputer what to do is called a program,
Each command in a program is called an instruction
A program written in machine language is referred to as machine code
ADD AX, BX
(Opcode)
(Destination operand)
(Source operand )

## Slide 3: Instructions
; COMMENT
Does not generate any machine code
LABEL: INSTRUCTION
Address identifier
Ex. START: MOV AX, BX
; copy BX into AX
There is a one-to-one relationship between assembly and machine language instructions
A compiled machine code implementation of a program written in a high-level language results in inefficient code
– More machine language instructions than an assembled version of an equivalent handwritten assembly language program

## Slide 4
Two key benefits of assembly language programming
  It takes up less memory
  It executes much faster

## Slide 5: Applications
One of the
most
beneficial
Assembly language
programming
uses of
real-time applications.
Real time means the task required by the application must be completed before any other input to the program that will alter its operation can occur
For example the device service routine which controls the operation of the floppy disk drive is a good example that is usually written in assembly language

## Slide 6
Assembly controlling
language not only hardware devices
good for but also
performing pure software operations
Code translation from ASCII to EBCDIC
Table sort routines
MathemaSearching through a large table of data for a special string of characters
tical routines
Assembly language: perform real-time operations
High-level languages: used to write those parts that are not time critical

## Slide 7: Converting Assembly Language Instructions to Machine Code
•
•
An instruction can be coded with 1 to 6 bytes Byte 1 contains three kinds of information
– Opcode field (6 bits) specifies the operation (add, subtract, move)
– Register Direction Bit (D bit) Tells the register operand in REG field in byte 2 is source or destination operand
1: destination 0: source
- Data Size Bit (W bit) Specifies whether the operation will be performed on 8-bit or 16-bit data
0: 8 bits 1: 16 bits

## Slide 8
Byte 2 has three fields
Mode field (MOD)
Register field (REG) used to identify the register for the first operand
Register/memory field (R/M field)

## Slide 9: Data Transfer Instructions - MOV
9
Mnemonic | Meaning | Format | Operation | Flags affected
MOV | Move | Mov D,S | (S) ◊ (D) | None
Destination Source
Accumulator Memory
Memory Accumulator
Register Register Memory Register Memory Seg reg Seg reg Reg 16 Memory
Register Memory Register Immediate Immediate Reg 16
Mem 16 Seg reg
Seg reg
NO MOV
Memory Immediate
Segment Register
Memory
Segment Register Segment Register
EX: MOV AL, BL

## Slide 10: Data Transfer Instructions - XCHG
Mnemonic Meaning Format Operation Flags affected
XCHG Exchange XCHG D,S (S) (D) None
Destination Source
Accumulator Reg 16
Memory Register
Register Register
Register Memory
Example: XCHG START [BX]
NO XCHG
MEMs SEG REGs

## Slide 11: Data Transfer Instructions – LEA, LDS, LES
Mnemo Meaning Format Operation nic
Flags affected
LEA
LEA Reg16,EA EA ◊ (Reg16)
None
LDS
Load Effective Address
Load Register And DS
LDS Reg16,MEM
(MEM) ◊
(Mem+2)
(Reg16)
(DS)
None
LES
Load Register and ES
LES Reg16,MEM
(MEM) ◊
(Reg16)
(Mem+2)
(ES)
None
LEA SI DATA
(or) MOV SI Offset DATA

## Slide 12: The XLAT Instruction
Mnemonic Meaning Format Operation Flags
XLAT Translate XLAT ((AL)+(BX)+(DS)0) ◊ (AL) None
Example:
Assume (DS) = 0300H, (BX)=0100H, and (AL)=0DH
XLAT replaces contents of AL by contents of memory location with
PA=(DS)0 +(BX) +(AL)
= 03000H + 0100H + 0DH = 0310DH
Thus
(0310DH) ◊ (AL)

## Slide 13: Arithmetic Instructions: ADD, ADC, INC, AAA, DAA
Mnemonic
Meaning
Format
Operation
Flags affected
ADD
Addition
ADD D,S
ALL
ADC
Add with carry
ADC D,S
(D)
(S)+(D) ◊ (D)
carry ◊ (CF)
(S)+(D)+(CF)
carry ◊
(CF)
ALL
INC | Increment by one | INC D | (D)+1 ◊ (D) | ALL but CY
AAA | ASCII adjust for addition | AAA | After addition AAA instruction is used to make sure the result is the correct unpacked BCD | AF,CF
DAA | Decimal adjust for addition | DAA | Adjust AL for decimal Packed BCD | ALL

## Slide 14: Examples:
Ex.1
ADD AX,2 ADC AX,2
Ex.2
INC BX
INC WORD PTR [BX]
Ex.3 ASCII CODE 0-9 = 30-39h
ADD CL,DL
MOV AL,CL
AAA
; [CL]=32=ASCII FOR 2
; [DL]=35=ASCII FOR 5
; RESULT[CL]=67
;Move the ascii result into AL since AAA adjust only [AL]
;[AL]=07, unpacked BCD for 7.

## Slide 15: Arithmetic Instructions – SUB, SBB, DEC, AAS, DAS, NEG
Mnemonic | Meaning | Format | Operation | Flags affected
SUB | Subtract | SUB D,S | (D) - (S) ◊ (D) | All
SBB | Subtract with borrow | SBB D,S | (D) - (S) - (CF) ◊ (D) | All
DEC | Decrement | DEC D | (D) - 1 ◊ (D) | All but CF
Borrow
(CF)
NEG
by one Negate
NEG D
All
DAS
DAS
Convert the result in AL to packed decimal format
All
AAS
Decimal adjust for subtraction
ASCII
adjust for subtraction
AAS
(AL) difference (AH) dec by 1 if borrow
CY,AC

## Slide 16: Multiplication and Division
1
6

## Slide 17: Multiplication and Division
17

## Slide 18: Multiplication and Division
Operand (Multiplier)
Result
Register or memory
AX
Multiplication Multiplicand (MUL or IMUL)
Byte*Byte AL
Word*Word AX
Register or memory
DX :AX
Dword*Dword
EAX
Register or memory
EAX :EDX
Division (DIV or IDIV)
Dividend
Operand (Divisor)
Quotient: Remainder
Word/Byte
AX
Register or Memory
AL : AH
Dword/Word
DX:AX
Register or Memory
AX : DX
Qword/Dword
EDX: EAX
Register or Memory
EAX : EDX

## Slide 19: Multiplication and Division Examples
•
4. IDIV BL →
=
1B
02
Ex1: Assume that each instruction starts from these values: AL = 85H, BL = 35H, AH = 0H
MUL BL → AL . BL = 85H * 35H = 1B89H → AX = 1B89H
IMUL BL → AL . BL = 2’S AL * BL = 2’S (85H) * 35H
= 7BH * 35H = 1977H→ 2’s comp → E689H → AX.
AH AL
DIV BL → AX = 0085H = 02 (85-02*35=1B) →
35H
BL 35H
AX 0085H
BL =
1B 02
AH AL

## Slide 20: Ex2: AL = F3H, BL = 91H, AH = 00H
1. MUL BL → AL * BL = F3H * 91H = 89A3H → AX = 89A3H
2. IMUL BL → AL * BL = 2’S AL * 2’S BL = 2’S (F3H) * 2’S(91H) =
0DH * 6FH = 05A3H → AX.
3.IDIV BL →
BL
AX =
2' S (91H )
00F 3H
6FH
00F 3H
= = 2→ (00F3 – 2*6F=15H)
AH AL | 
15 | 02
R Q | 
NEG
POS =
→ 2’s(02) = FEH→
AH AL | 
15 | FE
→
NEG
= 01→(F3-1*91=62) →
4. DIV BL → =
BL
AX
91H
00F 3H
AH AL | 
62 | 01
R Q | 

## Slide 21: Ex3: AX= F000H, BX= 9015H, DX= 0000H
DX AX | 
8713 | B000
DX AX | 
06FE | B000
3. DIV BL =
= B6DH → More than FFH → Divide Error.
15H
1. MUL BX = F000H * 9015H =
2. IMUL BX = 2’S(F000H) * 2’S(9015H) = 1000 * 6FEB =
F 000H
4. IDIV BL →
= C3H > 7F → Divide Error.
15H
2' S (F 000H )
1000H
= 15H

## Slide 22: Ex4:
AX= 1250H, BL= 90H
AX
1. IDIV BL → BL =
90H
1250H
POS POS
= NEG = 2' sNEG
=
2' s(90H )
1250H
1250H
= 70H
= 29H (Q) → (1250 – 29 * 70) = 60H (REM)
29H ( POS) → 2’S (29H) = D7H →
R Q | 
60H | D7H
= 20H→1250-20*90 =50H →
2. DIV BL → =
BL
AX
90H
1250H
R Q | 
50H | 20H
AH AL | 

## Slide 23: Logical Instructions
Format
Operation
Flags Affected
OR
XOR
NOT
Mnemonic Meaning AND Logical AND
Logical Inclusive OR
Logical Exclusive OR
LOGICAL NOT
AND D,S
OR D,S
XOR D,S
NOT D
(S) · (D) → (D)
(S)+(D) → (D)
(D)→(D)
_
(D) → (D)
OF, SF, ZF, PF, CF
AF undefined OF, SF, ZF, PF,
CF
AF undefined OF, SF, ZF, PF, CF
AF undefined None
(S)+
Destination Source
Register Register Memory Register Memory Accumulator
Register Memory Register Immediate Immediate Immediate
Destination
Register Memory

## Slide 24: LOGICAL Instructions
AND
  Uses any addressing mode except memory-to-memory and segment registers
  Especially used in clearing certain bits (masking) xxxx xxxx AND 0000 1111 = 0000 xxxx
(clear the first four bits)
– Examples:
AND BL, 0FH AND AL, [345H]
OR
– Used in setting certain bits
xxxx xxxx OR 0000 1111 = xxxx 1111 (Set the upper four bits)

## Slide 25
XOR
– Used in Inverting bits
xxxx xxxx XOR 0000 1111 = xxxxx’x’x’x’
-Example: Clear bits 0 and 1, set bits 6 and 7, invert bit 5 of register CL:
AND CL, OFCH | ; | 1111 1100B
OR CL, 0C0H | ; | 1100 0000B
XOR CL, 020H | ; | 0010 0000B

## Slide 26: Shift and Rotate Instructions
SHL/SAL: shift logical left/shift arithmetic left
SHR: shift logical right
SAR: shift arithmetic right
ROL: rotate left
ROR: rotate right
RCL: rotate left through carry
RCR: rotate right through carry

## Slide 27: Logical vs Arithmetic Shifts
A logical shift fills the newly created bit position with zero:
An arithmetic shift fills the newly created bit position with a copy of the number’s sign bit:

## Slide 28: Shift Instructions
Mnemonic | Meaning | Format | Operation | Flags Affected
SAL/SHL | Shift arithmetic Left/shift Logical left | SAL/SHL D, Count | Shift the (D) left by the number of bit positions equal to count and fill the vacated bits positions on the right with zeros | CF,PF,SF,ZF AF undefined OF undefined if count ≠1
SHR | Shift | SHR D, Count | Shift the (D) right by the number of bit positions | CF,PF,SF,ZF AF undefined
 | logical right |  | equal to count and fill the vacated bits positions on the left with zeros | OF undefined if count ≠1
SAR
Shift arithmetic right
SAR D, Count
Shift the (D) right by the
Number of bit positions equal to count and fill the
vacated bits positions on the left with the original most significant bit
CF,PF.SF.ZF
AF undefined OF undefined if count ≠1

## Slide 29: Allowed operands
Destination Count
Register 1
Register CL
Memory 1
Memory CL

## Slide 30
30

## Slide 31: SHL Instruction
31
The SHL (shift left) instruction performs a logical left shift on the destination operand, filling the lowest bit with 0.
•
Operand types: SHL reg,imm8 SHL mem,imm8 SHL reg,CL SHL mem,CL

## Slide 32: Fast Multiplication
mov dl,5
shl dl,1
Shifting left 1 bit multiplies a number by 2
shl dl,2
; DL = 20
Shifting left n bits multiplies the operand by 2n
,le5, 5 * 22 = 20
Fomr oevxamdlp

## Slide 33
Ex.
; Multiply
AX by 10
SHL AX, 1 MOV BX, AX MOV CL,2 SHL AX,CL ADD AX, BX

## Slide 34: SHR Instruction
The SHR (shift right) instruction performs a logical right shift on the destination operand. The highest bit position is filled with a zero.
MOV | DL,80 | 
SHR | DL,1 | ; DL = 40
SHR | DL,2 | ; DL = 10
Shifting right n bits divides the operand by 2n

## Slide 35: SAR Instruction
SAR (shift arithmetic right) performs a right arithmetic shift on the destination operand.
An arithmetic shift preserves the number's sign.
MOV DL,-80 SAR DL,1
SAR DL,2
; DL = -10
; DL = -40

## Slide 36: Rotate Instructions
Mnemonic | Meaning | Format | Operation | Flags Affected
ROL | Rotate Left | ROL D,Count | Rotate the (D) left by the number of bit positions equal to Count. Each bit shifted out from the left most bit goes back into the rightmost bit position. | CF OF undefined if count ≠ 1
ROR | Rotate Right | ROR D,Count | Rotate the (D) right by the number of bit positions equal to Count. Each bit shifted out from the rightmost bit goes back into the leftmost bit position. | CF OF undefined if count ≠ 1
RCL | Rotate Left through Carry | RCL D,Count | Same as ROL except carry is attached to (D) for rotation. | CF OF undefined if count ≠ 1
RCR | Rotate right through Carry | RCR D,Count | Same as ROR except carry is attached to (D) for rotation. | CF OF undefined if count ≠ 1 36

## Slide 37: ROL Instruction
ROL (rotate) shifts each bit to the left
The highest bit is copied into both the Carry flag and into the lowest bit
No bits are lost
MOV | Al,11110000b |  |  | 
ROL | Al,1 | ; | AL | = 11100001b
MOV | Dl,3Fh |  |  | 
ROL | Dl,4 | ; | DL | = F3h

## Slide 38: ROR Instruction
•
•
•
ROR (rotate right) shifts each bit to the right
The lowest bit is copied into both the Carry flag and into the highest bit
No bits are lost
MOV | AL,11110000b | 
ROR | AL,1 | ; AL = 01111000b
MOV | DL,3Fh | 
ROR | DL,4 | ; DL = F3h

## Slide 39: RCL Instruction
•
•
•
RCL (rotate carry left) shifts each bit to the left Copies the Carry flag to the least significant bit Copies the most significant bit to the Carry flag
CF
CLC |  | ; | CF = | 0 | 
MOV | BL,88H | ; | CF,BL | = | 0 10001000b
RCL | BL,1 | ; | CF,BL | = | 1 00010000b
RCL | BL,1 | ; | CF,BL | = | 0 00100001b
39

## Slide 40: RCR Instruction
•
•
•
RCR (rotate carry right) shifts each bit to the right Copies the Carry flag to the most significant bit Copies the least significant bit to the Carry flag
STC |  | ; | CF = | 1 | 
MOV | AH,10H | ; | CF,AH | = | 00010000 1
RCR | AH,1 | ; | CF,AH | = | 10001000 0

## Slide 41: Rotate Instructions
Destination Count
Register 1
Register CL
Memory 1
Memory CL

## Slide 42: Flag control instructions
MEANING
OPERATION
(CF) ⇓ 0
(CF) ⇓ 1
(CF) ⇓ (CF)l
Flags Affected
CF CF CF
MNEM- ONIC
CLC Clear Carry Flag STC Set Carry Flag
CMC Complement
Carry Flag
CLD Clear Direction
Flag
STD Set Direction Flag
(DF) ⇓ 0
SI & DI will be auto incremented while DF string instructions are executed.
(DF) ⇓ 1
SI &
DI will be auto decremented DF
while string instructions are executed. (IF) ⇓ 0
IF
CLI Clear Interrupt
Flag
STI Set Interrupt Flag
(IF) ⇓ 1
IF
42

## Slide 43: Compare Instruction, CMP
Mnemonic Meaning Format Operation
Flags Affected
CMP Compare CMP D,S
(D) – (S) is used in setting or resetting the flags
CF, AF, OF, PF, SF, ZF
(D) = (S)
(D) > (S)
(D) < (S)
; ZF=0
; ZF=0, CF=0
; ZF=0, CF=1
Allowed Operands
Source
Destination RegisterRegister RegisterMemory Memory
Register
RegisterImmediate
Memory Accumulator
Immediate Immedia4te3

## Slide 44: String?
44
An array of bytes or words located in memory
Supported String Operations
  Copy (move, load)
  Search (scan)
  Store
  Compare

## Slide 45: String Instruction Basics
45
Source DS:SI, Destination ES:DI
  You must ensure DS and ES are correct
  You must ensure SI and DI are offsets into DS and ES respectively
Direction Flag (0 = Up, 1 = Down)
CLD - Increment addresses (left to right)
STD - Decrement addresses (right to left)

## Slide 46: String Instructions
Instruction prefixes
Prefix
REP
REPE/REPZ
REPNE/REP NZ
Used with
MOVS STOS
CMPS SCAS
CMPS SCAS
Meaning
Repeat while not end of string CX ≠ 0
Repeat while not end of string and strings are equal. CX ≠ 0 and ZF = 1
Repeat while not end of string and strings are not equal. CX ≠ 0 and ZF = 0

## Slide 47: Instructions
Mnemonic meaning
format
Operation
MOVS
Move string DS:SI
ES:DI
MOVSB/ MOVSW
((ES)0+(DI)) ⇓ ((DS)0+(SI)) (SI) ⇓ (SI) ± 1 or 2
(DI) ⇓ (DI) ± 1 or 2
Flags effected
none
CMPS
Compare string
DS:SI
ES:DI
CMPSB/ CMPSW
Set flags as per ((DS)0+(SI)) - ((ES)0+(DI)) (SI) ⇓ (SI) ± 1 or 2
(DI) ⇓ (DI) ± 1 or 2
All status flags

## Slide 48
Mnemonic | meaning | format | Operation
SCAS | Scan string | SCASB/ | Set flags as per
 | AX – ES:DI | SCASW | (AL or AX) - ((ES)0+(DI))
 |  |  | (DI) ⇓ (DI) ± 1 or 2
LODS | Load string DS:SI ◊ AX | LODSB/ LODSW | (AL or AX) ⇓ ((DS)0+(SI)) (SI) ⇓ (SI) ± 1 or 2
STOS | Store string ES:DI ⇓ AX | STOSB/ STOSW | ((ES)0+(DI)) ⇓ (AL or A) ± 1 or 2 (DI) ⇓ (DI) ± 1 or 2

## Slide 49: Branch group of instructions
Branch instructions provide lot of convenience to the programmer to perform operations selectively, repetitively etc.
Branch group of instructions
Conditional jumps
Uncondi- tional jump
Iteration instructions
CALL
instructions
Return instructions

## Slide 50: SUBROUTINE & SUBROUTINE HANDILING INSTRUCTIONS
Call subroutine A
Next instruction
Call subroutine A
Next instruction
First Instruction
Return
Main program
Subroutine A

## Slide 51: A subroutine is a special segment of program that can be called for execution from any point in a program.
♣
♣
♣
♣
♣
♣
♣
An assembly language subroutine is also referred to as a “procedure”.
Whenever we need the subroutine, a single instruction is inserted in to the main body of the program to call subroutine.
To branch a subroutine the value in the IP or CS and IP must be modified.
After execution, we want to return the control to the instruction that immediately follows the one called the subroutine i.e., the original value of IP or CS and IP must be preserved.
Execution of the instruction causes the contents of IP to be saved on the stack. (this time (SP) ⇓ (SP) -2 )
A new 16-bit (near-proc, mem16, reg16 i.e., Intra Segment) value which is specified by the instructions operand is loaded into IP.
♣
Examples:
CALL 1234H CALL BX CALL [BX]

## Slide 52
•
Inter Segment
At starting CS and IP placed in a stack.
New values are loaded in to CS and IP given by the operand.
After execution original CS, IP values placed as it is.
Far-proc Memptr32
These two words (32 bits) are loaded directly into IP and CS with execution at CALL instruction.
First 16 ◊ IP Next 16 ◊ CS

## Slide 53: Meaning
53
Mnemonic
Format
Operation
Flags Affected
CALL
Subroutine call
CALL operand
Execution continues from
the address of the
none
subroutine specified by the operand. Information required to return back to the main program such as IP and CS are saved on the stack.
Operand
Near-proc Far – proc Memptr 16
Regptr 16
Memptr 32

## Slide 54: RETURN
54
•
Every subroutine must end by executing an instruction that returns control to the main program. This is the return (RET) instruction.
•
By execution the value of IP or IP and CS that were saved in the stack to be returned back to their corresponding regs. (this time (SP) ⇓ (SP)+2 )
Mnemonic | Meaning | Format | Operation |  |  | Flags
RET | Return | RET or | Return to | the | main | Affected None
RET operand
program by restoring IP (and CS for far-proc). If operands is present, it is added to the contents of SP.
Operand
None Disp16

## Slide 55: Loop Instructions
These instructions are used to repeat a set of instructions several times.
•
•
•
•
Format: LOOP Short-Label Operation: (CX) ⇓ (CX)-1
Jump is initialized to location defined by short label if CX≠0. otherwise, execute next sequential instruction.
Instruction LOOP works w.r.t contents of CX. CX must be preloaded with a count that represents the number of times the loop is to be repeat.
•
•
•
Whenever the loop is executed, contents at CX are first decremented then checked to determine if they are equal to zero.
If CX=0, loop is complete and the instruction following loop is executed.
If CX ≠ 0, content return to the instruction at the label specified in the loop instruction.

## Slide 56: LOOP Instruction contd.
General format : LOOP r8
; r8 is 8-bit signed value.
It is a 2 byte instruction.
Used for backward jump only.
Maximum distance for backward jump is only 128 bytes.
LOOP AGAIN is almost same as:
DEC CX JNZ AGAIN
LOOP instruction does not affect any flags.

## Slide 57
Mnemonic
meaning
format
Operation
LOOP
Loop
Loop short-label
(CX) ⇓ (CX) – 1
Jump to location given by short-label if CX ≠ 0
LOOPE/ LOOPZ
Loop while equal/ loop while zero
LOOPE/LOOPZ
short-label
(CX) ⇓ (CX) – 1
Jump to location given by short-label if CX ≠ 0 and ZF=1
LOOPNE/ LOOPNZ
Loop while not equal/ loop while not zero
LOOPNE/LOOPNZ
short-label
(CX) ⇓ (CX) – 1
Jump to location given by short-label if CX ≠ 0 and ZF=0

## Slide 58: Control flow and JUMP instructions
Unconditional Jump
Part 1
JMP AA
Unconditional JMP
Skipped part
AA
Part 3
XXXX
Part 2
Next instruction
JMP ◊ unconditional jump JMP Operand

## Slide 59: Unconditional Jump
59
Unconditional Jump Instruction
Far Jump or Inter segment Jump
(Jump to a different segment)
Near Jump or Intra segment Jump
(Jump within the segment)
Is limited to the address with in the current segment. It is achieved by modifying value in IP
Permits jumps from one code
segment to another. It is
achieved by modifying CS and IP
Operands
Short label Near label Far label Memptr16 Regptr16 memptr32
Inter Segment Jump
Inter Segment Jump

## Slide 60: Conditional Jump
Part 1
Jcc AA
Conditional Jump
Skipped part
XXXX
Part 3
AA XXXX
condition
YES
Part 2
NO
Next instruction

## Slide 61: Conditional Jump instructions
Conditional Jump instructions in 8086 are just 2 bytes long. 1-byte opcode followed by 1-byte signed displacement (range of –128 to
+127).
Conditional Jump Instructions
Jumps based on a single flag
Jumps based on more than one flag

## Slide 62: Conditional Jump Instructions
Mnemonic : Meaning : Format : Operation :
Flags affected :
Jcc
Conditional Jump Jcc operand
If condition is true jump to the address specified by operand. Otherwise the next instruction is executed.
None

## Slide 63: TYPES
63
Mnemonic | meaning | condition
JA | Above | CF=0 and ZF=0
JAE | Above or Equal | CF=0
JB | Below | CF=1
JBE | Below or Equal | CF=1 or ZF=1
JC | Carry | CF=1
JCXZ | CX register is Zero | (CF or ZF)=0
JE | Equal | ZF=1
JG | Greater | ZF=0 and SF=OF
JGE | Greater or Equal | SF=OF
JL | Less | (SF XOR OF) = 1

## Slide 64
Mnemonic
JLE
JNA JNAE JNB JNBE JNC JNE JNG JNGE
condition
((SF XOR OF) or ZF) = 1 CF =1 or Zf=1
CF = 1
CF = 0
CF = 0 and ZF = 0 CF = 0
ZF = 0
((SF XOR OF) or ZF)=1 (SF XOR OF) = 1
JNL
meaning
Less or Equal Not Above
Not Above nor Equal
Not Below
Not Below nor Equal Not Carry
Not Equal
Not Greater
Not Greater nor Equal
Not Less
SF = OF

## Slide 65
Mnemonic | meaning | condition
JNLE | Not Less nor Equal | ZF = 0 and SF = OF
JNO | Not Overflow | OF = 0
JNP | Not Parity | PF = 0
JNZ | Not Zero | ZF = 0
JNS | Not Sign | SF = 0
JO | Overflow | OF = 1
JP | Parity | PF = 1
JPE | Parity Even | PF = 1
JPO | Parity Odd | PF = 0
JS | Sign | SF = 1
JZ | Zero | ZF = 1

## Slide 66: Jumps Based on a single flag
JZ | r8 | ;Jump if zero flag set to 1 (Jump if result is zero)
JNZ | r8 | ;Jump if Not Zero (Z flag = 0 i.e. result is nonzero)
JS | r8 | ;Jump if Sign flag set to 1 (result is negative)
JNS | r8 | ;Jump if Not Sign (result is positive)
JC | r8 | ;Jump if Carry flag set to 1
JNC r8 ;Jump if No Carry There is no jump based on AC flag |  | 
JP | r8 | ;Jump if Parity flag set to 1 (Parity is even)
JNP | r8 | ;Jump if No Parity (Parity is odd)
JO | r8 | ;Jump if Overflow flag set to 1 (result is wrong)
JNO | r8 | ;Jump if No Overflow (result is correct)

## Slide 67
JZ r8 ; JE (Jump if Equal) also means same.
JNZ r8 ; JNE (Jump if Not Equal) also means same.
JC r8 ;JB (Jump if below) and JNAE (Jump if Not Above or Equal) also mean same.
JNC r8 ;JAE (Jump if Above or Equal) and JNB (Jump if Not Above) also mean same.
JZ, JNZ, JC and JNC used after arithmetic operation
JE, JNE, JB, JNAE, JAE and JNB are used after a compare operation.
JP r8 ; JPE (Jump if Parity Even) also means same. JNP r8 ; JPO (Jump if Parity Odd) also means same.

## Slide 68: Examples for JE or JZ instruction
Ex. for forward jump (Only examples for JE given)
CMP SI, DI
JE SAME
Should be
<=127
bytes
ADD CX, DX
;Executed if Z = 0
:
(if SI not equal to DI)
:
SAME:
SUB BX, AX
;Executed if Z = 1
(if SI = DI)

## Slide 69: Examples for JE or JZ instruction
Ex. for backward jump
BACK:
Should be
<= 128
bytes
; executed if Z = 1 (if SI = DI)
SUB BX, AX
:
: CMP SI, DI JE BACK ADD CX, DX
;executed if Z = 0
(if SI not equal to DI)

## Slide 70: Jumping beyond -128 to +127?
What if
>127
bytes
NEXT:
SAME:
Requirement CMP SI, DI JE SAME ADD CX, DX
:
: SUB BX, AX
SAME:
Then do this! CMP SI, DI JNE NEXT JMP SAME ADD CX, DX
:
: SUB BX, AX
Range for JMP (unconditional jump) can be +215 = + 32K JMP instruction discussed in detail later

## Slide 71: Terms used in comparison
Above and Below used for comparing Unsigned nos. Greater than and less than used with signed numbers. All Intel microprocessors use this convention.
95H is above 65H | Unsigned comparison - | True
95H is less than 65H | Signed comparison - | True
95H is negative, 65H is positive
65H is below 95H | Unsigned comparison - | True
65H is greater than 95H | Signed comparison - | True

## Slide 72: Jump on multiple flags
Conditional Jumps based on more than one flag are used after a CMP (compare) instruction.
JBE or JNA
Jump if Below or Equal Jump if Not Above
Jump if | No Jump if | Ex.
Cy = 1 OR Z= 1 | Cy = 0 AND Z = 0 | CMP BX, CX
Below OR Equal | Surely Above | JBE BX_BE
BX_BE (BX is Below or Equal) is a symbolic location

## Slide 73: Jump on multiple flags contd.
JNBE or JA
Jump if Not (Below or Equal) Jump if Above
Jump if | No Jump if | Ex.
Cy = 0 AND Z= 0 | Cy = 1 OR Z = 1 | CMP BX, CX
Surely Above | Below OR Equal | JA BXabove
BXabove (BX is above) is a symbolic location

## Slide 74: Jump on multiple flags contd.
JLE or JNG
Jump if Less than OR Equal Jump if Not Greater than
Jump if
S = 1 AND V = 0
(surely negative) OR (S = 0 AND V = 1)
(wrong answer positive!) OR Z = 1 (equal)
i.e. S XOR V = 1 OR Z = 1
No Jump if
S = 0 AND V = 0
(surely positive) OR (S = 1 AND V = 1)
(wrong answer negative!) AND Z = 0 (not equal)
i.e. S XOR V = 0 AND Z = 0

## Slide 75: Jump on multiple flags contd.
JNLE or JG
Jump if Not (Less than OR Equal) Jump if Greater than
Jump if
No Jump if
S = 0 AND V = 0
(surely positive) OR (S = 1 AND V = 1)
(wrong answer negative!) AND Z = 0 (not equal)
i.e. S XOR V = 0 AND Z = 0
S = 1 AND V = 0
(surely negative) OR (S = 0 AND V = 1)
(wrong answer positive!) OR Z = 1 (equal)
i.e. S XOR V = 1 OR Z = 1

## Slide 76: Jump on multiple flags contd.
JL or JNGE
Jump if Less than
Jump if Not (Greater than OR Equal)
Jump if
S = 1 AND V = 0
(surely negative) OR (S = 0 AND V = 1)
(wrong answer positive!)
i.e. S XOR V = 1
When S = 1, result cannot be 0
No Jump if
S = 0 AND V = 0
(surely positive) OR (S = 1 AND V = 1)
(wrong answer negative!)
i.e. S XOR V = 0
When S = 0, result can be 0

## Slide 77: Jump on multiple flags contd.
JNL or JGE
Jump if Not Less than
Jump if Greater than OR Equal
Jump if
S = 0 AND V = 0
(surely positive) OR (S = 1 AND V = 1)
(wrong answer negative!)
i.e. S XOR V = 0
When S = 0, result can be 0
No Jump if
S = 1 AND V = 0
(surely negative) OR (S = 0 AND V = 1)
(wrong answer positive!)
i.e. S XOR V = 1
When S = 1, result cannot be 0

## Slide 78: Near Jump
Near Jump
Direct Jump (common)
Indirect Jump (uncommon)
Short Jump
Long Jump
2 or more bytes Starting with FFH
Range: complete segment
2 bytes
3 bytes
EB r8
E9 r16
range + 27 range +215
3 Near Jump and 2 Far Jump instructions have the same mnemonic JMP but different opcodes

## Slide 79: Short Jump
2 byte (EB r8) instruction Range: -128 to +127 bytes
Backward jump: Assembler knows the quantum of jump. Generates Short Jump code if <=128 bytes is the required jump Generates code for Long Jump if >128 bytes is the required jump
Forward jump: Assembler doesn’t know jump quantum in pass 1. Assembler reserves 3 bytes for the forward jump instruction.
If jump distance turns out to be >128 bytes, the instruction is coded as E9 r16 (E9H = Long jump code).
If jump distance becomes <=128 bytes, the instruction is coded as EB r8 followed by code for NOP (E8H = Short jump code).

## Slide 80: Short Jump contd.
SHORT Assembler Directive
Assembler generates only 2 byte Short Jump code for forward jump, if the SHORT assembler directive is used.
SAME
Programmer should ensure that the Jump distance is <=127 bytes
SAME:
JMP SHORT
:
:
MOV CX, DX

## Slide 81: Long Jump
3-byte (E9 r16) instruction Range: -32768 to +32767 bytes
Long Jump can cover entire 64K bytes of Code segment
CS:0000H
Long Jump can handle it as jump quantum is
<=32767
CS:8000H
JMP FRWD
:
:
FRWD =
CS:FFFFH

## Slide 82: Long Jump contd.
It can cover entire 64K bytes of Code segment
Long Jump can handle it as jump quantum is
<=32768
BKWD =
CS:0000H
CS:8000H
JMP BKWD
:
:
CS:FFFFH

## Slide 83: Long Jump or Short Jump?
Can be treated as a small (20H) backward branch!
CS:0000H
Jump distance
=FFE0H. Too
very long
forward jump
CS:000DH CS:0010H
:
:
JMP FRWD
:
:
FRWD=
CS:FFF0H CS:FFFFH

## Slide 84: Long Jump or Short Jump?
Can be treated as a small (20H) forward branch!
CS:0000H
Jump distance
=FFE0H. Too
very long
backward jump
BKWD=
CS:0010H
:
:
:
:
JMP BKWD
CS:FFF0H CS:FFFFH

## Slide 85: Intra segment indirect Jump
Near Indirect Jump is uncommon. Instruction length: 2 or more bytes Range: complete segment
Ex.1: JMP DX
If DX = 1234H, branches to CS:1234H 1234H is not signed relative displacement
Ex. 2: JMP wordptr 2000H[BX]
BX | 1234H | DS:3234H | 5678H | Branches to
 |  | DS:3236H | AB22H | CS:5678H

## Slide 86: Far Jump
Far Jump
Direct Jump (common)
Indirect Jump (uncommon)
5 bytes
2 or more bytes Starting with FFH Range: anywhere
EA,2 byte offset, 2 byte segment
Range: anywhere
3 Near Jump and 2 Far Jump instructions have the same mnemonic JMP but different opcodes

## Slide 87: Inter segment Direct Jump
Also called Far Direct Jump
It is the common inter segment jump scheme
It is a 5 byte instruction 1 byte opcode (EAH)
2 byte offset value
2 byte segment value
Ex. JMP Far ptr LOC

## Slide 88: Inter segment Indirect Jump
Instruction length depends on the way jump location is specified
It can be a minimum of 2 bytes
Ex. JMP DWORD PTR 2000H[BX]

## Slide 89: Inter segment Indirect Jump
Also called Far Indirect Jump It is not commonly used
Instruction length is a minimum of 2 bytes.
It depends on the way jump location is specified
Ex. JMP DWORD PTR 2000H[BX]
BX | 1234H | Branches to ABCDH:5678H
DS:3234H | 5678H | It is a 4-byte instruction
DS:3236H | ABCDH | 

## Slide 90: Machine control instructions
HLT instruction – HALT processing
the HLT instruction will cause the 8086 to stop fetching and executing instructions. The 8086 will enter a halt state. The only way to get the processor out of the halt state are with an interrupt signal on the INTR pin or an interrupt signal on NMI pin or a reset signal on the RESET input.
NOP instruction
this instruction simply takes up three clock cycles and does no processing. After this, it will execute the next instruction. This instruction is normally used to provide delays in between instructions.
ESC instruction
whenever this instruction executes, the microprocessor does NOP or access a data from memory for coprocessor. This instruction passes the information to 8087 math processor. Six bits of ESC instruction provide the opcode to coprocessor.
when 8086 fetches instruction bytes, co-processor also picks up these bytes and puts in its queue. The co-processor will treat normal 8086 instructions as NOP. Floating point instructions are executed by 8087 and during this 8086 will be in WAIT.

## Slide 91: Machine control instructions contd
LOCK instruction
this is a prefix to an instruction. This prefix makes sure that during execution of the instruction, control of system bus is not taken by other microprocessor.
in multiprocessor systems, individual microprocessors are connected together by a system bus. This is to share the common resources. Each processor will take control of this bus only when it needs to use common resource.
the lock prefix will ensure that in the middle of an instruction, system bus is not taken by other processors. This is achieved by hardware signal ‘LOCK’ available on one of the CPU pin. This signal will be made active during this instruction and it is used by the bus control logic to prevent others from taking the bus.
once this instruction is completed, lock signal becomes inactive and microprocessors can take the system bus.
WAIT instruction
this instruction takes 8086 to an idle condition. The CPU will not do any processing during this. It will continue to be in idle state until TEST pin of 8086 becomes low or an interrupt signal is received on INTR or NMI. On valid interrupt, ISR is executed and processor enters the idle state again.